## Slide 1
GAIN
MIX
LEVEL
TIME
FDBK
Filter
BYPASS
Match
Klone
Mesa
MARS
Amp Modeller/
Delay
Proteus
Ameri
Rectify
Norm
Dot 8th
Triplett
Amp
Cab
Delay
Gain: Amount of input gain
Mix: Dry Amp to Delay mix
Level: Overall output volume
Filter: Lowpass left of center, highpass right of center
Time: Delay time 0 to 2 seconds
FDBK: Delay feedback
Amp Switch (neural model select):
Left: Matchless SC30
Center: Klon clone
Right: Mesa iib+
Cab Switch (IR Select):
Left: Proteus IR (from plugin)
Center: American style IR
Right: Rectifier style IR
Delay Mode Switch:
Left: Normal delay
Center: Dotted 8th added
Right: Triplett added
Dip Switches:
1: Neural Model On/Off
2: IR On/Off
Left Footswitch: Bypass/Engage
Right Footswitch: Hold to save preset. Press to engage/disengage preset. Saves between power cycles.
Mars is an Amp Modeler / Delay pedal that uses neural networks to model the distortion stage of an amp or pedal.
Mono In/Out Processing
If using TRS, only takes left channel for input, and copies Left to Right for output
Expression: YES
MIDI: NO
PRESET

## Slide 2
Decay
MIX
(R/D)
Time
Damp
FDBK
Mod
(Rate)
BYPASS / ALT
Factory
Hall
Cloud
NEPTUNE
REVERB/DELAY
D+->R
D||R
D->R
NORM
OCT
REV
Reverb
Routing
Delay
PRESET
Decay: Length of reverb decay
Mix: Dry/Effect mix, alt is Reverb/Delay volume ratio
Time: Delay time 0 to 4 seconds (2 seconds max for octave, double speed)
Mod (Rate): Modulation amount of the reverb, alt is the modulation rate
Damp: Lowpass filter for the reverb (damping)
FDBK: Delay feedback
Reverb Switch
Left: Factory Chorus Reverb
Center: Hall (Medium space)
Right: Cloud (RubiKa)
Routing Switch
Left: Some delay into reverb
Center: Parallel delay / reverb
Right: Delay into reverb
Delay Mode Switch:
Left: Normal delay
Center: Octave delay
Right: Reverse Delay
Dip Switches:
1: Stereo / MISO (Mono in Stereo out)
2: N/A
Left Footswitch: Bypass/Engage, hold to engage alternate mode (indicated by dimmed LED)
Neptune is a Reverb/Delay pedal capable of ethereal sounds.
Stereo In/Out Processing
(MISO or Stereo)
Expression: YES
MIDI: YES
Right Footswitch: Hold to save preset. Press to engage/disengage preset. Saves between power cycles.

## Slide 3
Decay
Low Freq
High Freq
Low Shelf
High Shelf
Mix
BYPASS
Low
Med
High
Jupiter
REVERB
Lushness
Modulation
PreDelay
PRESET
Decay: Length of reverb decay, exponential taper, ~300ms to 60 seconds.
Low Freq: Low Shelf cutoff frequency, full left lets everything through
High Freq: High Shelf cutoff frequency, full right lets everything through
Mix: Dry/Wet mix knob
Low Shelf: Low shelf filter gain cut, left is inf, right is 0.0Db gain
High Shelf: High shelf filter gian cut, left is inf, right is 0.0Db gain
Lushness Switch
Left: Low lush, delay-like reverb
Center: Medium lushness
Right: High, lots of diffusion
Modulation Switch
Left: Low mod amount/rate
Center: Med mod amount/rate
Right: High mod amount/rate
PreDelay:
Left: no predelay
Center: 100ms predelay
Right: 200ms predelay
Dip Switches:
1: Stereo / MISO (Mono in Stereo out)
2: N/A
Left Footswitch: Bypass/Engage, hold to engage alternate mode (indicated by dimmed LED)
Jupiter is a Reverb pedal with a focus on EQ for shaping unique and impossible spaces.
Stereo In/Out Processing
(MISO or Stereo)
Expression: YES
MIDI: YES
Low
Med
High
Low
Med
High
Right Footswitch: Hold to save preset. Press to engage/disengage preset. Saves between power cycles.

## Slide 4
Level A
Mod A
(R Time)
Level B
Mod B
(R Damp)
Speed B
Speed A
Loop A
Smooth
Step
Rand
Pluto
Dual Looper
Stability
Filter
Reverb
Norm
Single
Fripp
Speed Mode
Effect
Record Mode
Level A: Volume of Loop A, 0 to 2x
Mod A: Effect modifier for Loop A, or if reverb is selected, reverb time for both Loop A and B
Level B: Volume of Loop B, 0 to 2x
Speed A: Speed/Direction of Loop A
Mod B: Effect modifier for Loop B, or if reverb is selected, reverb time for both Loop A and B
Speed B: Speed/Direction of Loop B
Speed Mode:
Left: Smooth like a tape mode, reverse 2x to fwd 2x speed.
Center: Stepped in 5ths and Octaves from reverse 2x to forward 3x, noon is 1x speed
Right: TBD
Effect (Applied to loops):
Left: Stability, adds random variations in speed
Center: Filter, left of noon is lowpass, right is high
Right: Stereo reverb applied to both A/B loops
Record Mode Switch:
Left: Normal Record w/ repeated overdub
Center: Single record, starts at beginning of loop, stops recording at end of loop
Right: Frippertronics mode, delay-like loop with a decay while recording.
Dip Switches:
1: Stereo Looper/Dual Loopers
3: Expression Toggle (see Readme)
Left Footswitch: Loop A, press once to begin recording, press again to stop recording and start playback. Repeat to overdub. Hold to clear loop. Double tap to pause loop.
Pluto is a dual/stereo variable speed looper pedal with real-time effects. If Stereo is engaged, the two loops are synced (A=Left channel, B=Right channel). If Dual Looper is engaged, Loop A and B are completely separate. Loops are recorded to the current Speed setting, so if you record while at 2x it will sound normal, if you drop to 1x it will sound like half speed, etc.
Stereo/Miso: If using Dual looper, Left channel is copied to right for both Loop A and loop B. While in Stereo mode, Loop A is the left channel, Loop B is the right channel (Loop B footswitch is inactive).
- Pluto runs at 96kHz (instead of 48kHz)
Expression: YES
MIDI: YES (Knobs and Toggles, see Readme cc)
Loop B
Right Footswitch: Loop B, same action as Loop A. If Stereo dipswitch enabled, Loop B footswitch is inactive, and Pluto becomes a Stereo Looper. Loop B controls are applied to Right Channel, Loop A controls are applied to Left channel.

## Slide 5
Decay
Mix
Damp
Tone
Detune
Shimmer
BYPASS
-OCT
+OCT
Both
Venus
Spectral Reverb
Less
None
More
Less
None
More
Shim Mode
LoFi Mode
Drift
Decay: Length of decay time
Mix: Dry/Wet Mix
Damp: Amount of Dampening
Shimmer: Adds octave string-like shimmer based on Shimmer mode toggle
Tone: Adds octave + 5ths string-like shimmer
Detune: Right of noon shifts reverb pitch up over time, Left of noon shifts reverb pitch down over time, center is no detuning
Shimmer Mode Toggle
Left: Adds Octave Down
Center: Adds Octave Up
Right: Both Octave Up and Down
LoFi Mode Toggle:
Left: Less applies some samplerate reduction with a lowpass filter
Center: None – no samplerate reduction
Right: More applies more samplerate reduction without a lowpass filter
Drift Toggle: Oscillates all the knob controls (except mix) between the current setting and 0 at a slow rate ( between 25 and 50 second periods).
Left: Slow drift, Sine wave, lower rate
Center: No drift
Right: More drift, Triangle wave, higher rate
Dip Switches:
1,2,3,4: TBD (no action currently assigned to dip switches)
Left Footswitch: Bypass/Engage, hold more than a half second to enter/exit Set Expression mode. Hold for > 2 seconds to clear all expression settings.
Right Footswitch: Hold to Freeze the current reverb sound indefinitely.
Venus is a Spectral Reverb pedal that operates in the frequency domain to create lush soundscapes. Features string-like overtones, detuning, and spectral freeze.
Mono In/Out Processing
If using TRS, only takes left channel for input, and copies Left to Right for output
Expression: YES
MIDI: YES
FREEZE

## Slide 6
PreDelay
Mix
Filter
FDBK
DriftMod
Time
BYPASS
Rand
Saturn
Spectral Delay
Rand
Mode1
None
Mode2
Time Mode
FDBK Mode
Drift
PreDelay: Up to 2 seconds of predelay prior to spectral delay
Mix: Dry/Wet Mix
Filter: Low Pass to the left, Highpass to the right, applied to the delaylines
Time: Up to 4 second delay spread of the individual frequency bins.
FDBK: Feedback of the delay, behavior depends on the mode toggle.
DriftMod: Frequency of drift (0 to 1Hz)
Time Mode Toggle:
Left: Linear increase in delay from low to high frequencies
Center: Sine wave over low to high frequencies
Right: Random delay times for each frequency
Feedback Mode Toggle:
Left: Even, all delaylines have the same fdbk
Center: linear decrease with frequency
Right: Random FDBK values for each freq.
Drift Toggle (slow modulation of all the knobs excluding mix, from the current position to 0) :
Left: Predelay not included in drift modulation
Center: No Drift
Right: Adds Predelay to drift (wacky time stretching sounds)
Dip Switches:
1: Mono/Stereo (mono processes more freqs)
2: MISO (mono in stereo out) / Stereo
3: Stereo Spread Off/On
4: Adds Feedback to Predelay
Left Footswitch: Bypass/Engage, hold both footswitches more than a half second to enter/exit Set Expression mode. Hold both footswitches for > 2 seconds to clear all expression settings.
Right Footswitch: Hold to save preset of all knobs, toggles, and dipswitches. Press to engage/disengage preset. Saves between power cycles.
Saturn is a Spectral Delay pedal that splits your signal into frequency particles and delays each part separately. Like a prism refracting white light into colors, Saturn turns your guitar into a kaleidoscope of sounds.
Stereo In/Out Processing
Mono, MISO, and Stereo modes
Expression: YES
MIDI: YES
PRESET

## Slide 7
GAIN
LEVEL
PRESENCE
MID
TREBLE
BASS
BYPASS
Low
Med
High
Mercury
Amp Modeller
Amp 1
Amp 2
Amp 3
Amp
Cab
Gain: Amount of input gain
Level: Overall output volume
Presence: +10/-10 dB
Bass: +10/-10 dB
Mid: +10/-10 dB
Treble: +10/-10 dB
Amp Group
Left: Low Gain
Center: Med Gain
Right: High Gain
Model Select (depends on Toggle 1 group selection)*
Left: Amp 1
Center: Amp 2
Right: Amp 3
Left Footswitch: Bypass/Engage
Mercury is an Amp Emulator using Neural Amp Modeler (NAM).
Mono In/Out Processing
If using TRS, only takes left channel for input, and copies Left to Right for output
Expression: YES
MIDI: YES
*NAM Models
Low Gain:
- Matchless SC30
- Twin Reverb
- Dumble Low Gain (from kit build)
Medium Gain:
- Dumble Higher Gain (from kit build)
- Ethos Tube Pedal
- JCM800 Medium Gain
High Gain:
- Mesa iib
- Splawn
- PRS Archon

## Slide 8
PreDelay
Mix
Decay
Mod Rate
Filter
Mod
BYPASS
Small
Med
Big
Earth
Plate Reverb/
Octave
Size
Octave
Footswitch
Action
PreDelay: PreDelay up to around 700ms
Mix: Dry/Wet mix
Decay: Amount of decay of the reverb
Mod Depth: Intensity of reverb mod
Mod Rate: Speed of reverb mod
Filter: High and low cut filter in reverb tank.
Size Toggle
Left: Small size
Center: Medium size
Right: Big size
Octave Switch
Left: None
Center: Octave Up
Right: Octave Up and Down
Footswitch Action:
Left: Freeze (Decay set to 1)
Center: Overdrive the Reverb
Right: Momentary Octave (based on center toggle)
Dip Switches:
1: Diffusion Disabled (on to disable input diffusion)
2. Octave only mode (only sends octaves to reverb, no dry, when in octave mode)
Left Footswitch: Bypass/Engage
Earth is a digital Plate Reverb pedal with octave effects.
Mono in Stereo Out Processing (MISO)
Expression: YES
MIDI: YES
None
OctUp
OctUpDn
Freeze
OD
Oct
Right Footswitch: Do action based on 3rd toggle.

## Slide 9
Mix
LPF
REGEN
INT 1
(Speed)
INT 2
(Depth)
Glide
BYPASS / ALT
Quarter
Dot 8th
8th
Balnea
Digital Delay /
Pitch Shifter
Tap / Step
Mix: Dry/Wet Mix
LPF: Resonant Low Pass Filter Cuttoff
REGEN: Delay feedback / regen. Higher settings can oscillate out of control, very sensitive to LPF setting.
GLIDE: Pitch transition time between sequencer steps.
INT 1: Sets first interval in musical increments (by changing the delay time). Alt is Mod Speed)
INT 2: Sets Second interval in musical increments (by changing the delay time). Alt is Mod Depth
Intervals: -2Oct, -Oct and 5th, -Oct, -5th, -4th, Off, 4th, 5th, Oct, Oct and 5th, 2Oct
Base Sequencer Step Length
Left: Quarter Note (Same as Tap Tempo)
Center: Dotted Eighth Note
Right: Eighth Note
Dip Switches:
1: Stereo / Miso (off is MISO)
2: Reverse Mode
3. Dissonant Mode
4. Chromatic Mode (overrides Dissonant Mode)
Left Footswitch: Bypass/Engage, hold to engage alternate mode (indicated by dimmed LED)
Balnea is a Digital Delay And Pitch Shifter inspired by the Chase Bliss Thermae pedal. This design mostly follows the Thermae controls, minus the dipswitch modulation features and in depth customization. Because it’s digital however, it can do a few things Thermae can’t do, such as Stereo and Reverse Delay, and adds some unique interval modes. It leans into the crunchy side of digital audio time shifting and embraces aliasing and distortion, rather than trying to avoid it.
Stereo In/Out Processing
Expression: YES (controls LPF)
MIDI: YES
Midi Synth mode
Right Footswitch: Tap Tempo, or next sequencer step when in stepped mode. Hold to temporarily move Regen to max, “self oscillation runaway mode”.
Quarter
Dot 8th
8th
Quarter
Dot 8th
8th
INT 1 Step Length
Left: Quarter Note (Same as Tap Tempo)
Center: Dotted Eighth Note
Right: Eighth Note
INT 2 Step Length
Left: Quarter Note (Same as Tap Tempo)
Center: Dotted Eighth Note
Right: Eighth Note

## Slide 10
Knob 1
Knob 2
Knob 3
Knob 5
Knob 6
Knob 4
FootSw 1
Opt 1
Opt 2
Opt 3
FunBox
Opt 1
Opt 2
Opt 3
Opt 1
Opt 2
Opt 3
Toggle 1
Toggle 2
Toggle 3
Stereo ¼” In/Out Jacks
9v Center Negative Power
MIDI Input (1/8” TRS Jack)
Daisy Seed USB port
4 On/Off Dipswitches
Two Momentary Footswitches
with indication LEDs.
FunBox is a pedal platform designed around the Daisy Seed. Fits in a 125B enclosure.
FootSw 2
Expression
MIDI
USB
Expression Input (1/8” TRS Jack)
Three 3-way Toggles (On-Off-On)
6 Potentiometer Knobs
Specs:
Buffered Stereo In/Out Paths
Up to 96KHz, 24-bit Digital Processing
64MB SDRAM, 8MB Flash
ARM Cortex M7 480MHz
Expression and MIDI Inputs
Through Hole PCB
Digital Bypass only