## Slide 1
GAIN
MIX
LEVEL
TIME
FDBK
Filter
BYPASS
Match
Klone
Mesa
MARS
Amp Modeller/
Delay
Proteus
Ameri
Rectify
Norm
Dot 8th
Triplett
Amp
Cab
Delay
Gain: Amount of input gain
Mix: Dry Amp to Delay mix
Level: Overall output volume
Filter: Lowpass left of center, highpass right of center
Time: Delay time 0 to 2 seconds
FDBK: Delay feedback
Amp Switch (neural model select):
Left: Matchless SC30
Center: Klon clone
Right: Mesa iib+
Cab Switch (IR Select):
Left: Proteus IR (from plugin)
Center: American style IR
Right: Rectifier style IR
Delay Mode Switch:
Left: Normal delay
Center: Dotted 8th added
Right: Triplett added
Dip Switches:
1: Neural Model On/Off
2: IR On/Off
Left Footswitch: Bypass/Engage
Right Footswitch: TBD
Mars is an Amp Modeler / Delay pedal that uses neural networks to model the distortion stage of an amp or pedal.
Mono In/Out Processing
If using TRS, only takes left channel for input, and copies Left to Right for output

## Slide 2
Decay
MIX
R/D
Time
Damp
FDBK
Mod
(Rate)
BYPASS / ALT
Factory
Hall
Cloud
NEPTUNE
REVERB/DELAY
D+->R
D||R
D->R
NORM
OCT
REV
Reverb
Routing
Delay
FREEZE
Decay: Length of reverb decay
Mix: Dry/Effect mix, alt is Reverb/Delay volume ratio
Time: Delay time 0 to 4 seconds (2 seconds max for octave, double speed)
Mod (Rate): Modulation amount of the reverb, alt is the modulation rate
Damp: Lowpass filter for the reverb (damping)
FDBK: Delay feedback
Reverb Switch
Left: Factory Chorus Reverb
Center: Hall (Medium space)
Right: Cloud (Rubi Kai)
Routing Switch
Left: Some delay into reverb
Center: Parallel delay / reverb
Right: Delay into reverb
Delay Mode Switch:
Left: Normal delay
Center: Octave delay
Right: Reverse Delay
Dip Switches:
1: Stereo / MISO (Mono in Stereo out)
2: N/A
Left Footswitch: Bypass/Engage, hold to engage alternate mode (indicated by dimmed LED)
Right Footswitch: Freeze – holds the current delay/reverb feedback/decay
Neptune is a Reverb/Delay pedal capable of ethereal sounds.
Stereo In/Out Processing
(MISO or Stereo)